## Slide 1
Wang Liang
43th PRP ：Muon Source Based on the SHINE Facility
2024.3.18
–– Negative Muon Detection Scheme Study

## Slide 2
03.
Simulation Validity
06.
Summary and Outlook
01.
Motivation & Background
04.
Discussion on degrader
02.
μ- Detection Methods
05.
Detector deployment

## Slide 3
Motivation & Background
01

## Slide 4
Motivation
Muon’s life time only 2.2 μs
What Muon Can Do
μSR
CLFV
（Charged lepton flavor violation）
New collider
We Need A Muon Source!

## Slide 5
Background
But SHINE haven’t finished yet,
we can use SXFEL (Shanghai Soft X-ray Free Electron Laser)as an alternative
SHINE Facility is of Great Potential
SHINE’s (Shanghai High repetition rate XFEL and Extreme light facility) Parameter:
- 8GeV electron energy + 100 pC charge per bunch + repetition rate of 1MHz
Run Simulations
Test on SXFEL
Run on SHINE
- 1.6GeV electron energy + 500 pC charge per bunch + repetition rate of 10Hz
Our Scheme is as follows
Current Stage & μ- detection is my job

## Slide 6
μ- Detection Methods
02

## Slide 7
μ- Detection Methods
MuSic RCNP Settings
(Muon Science Innovative Channel)
Mechanism of muonic X-rays
Degrader(will be further discuss)
Reduce background particles, such as electrons.
Stopper:
Capture high momentum Muon and release Muonic X-ray.
Detector:
High resolution detector such as Ge （3%） or 7%） to record spectrum
Information about Muon intensity is contained in the μ X-ray
and it can be reflected through spectrum.

## Slide 8
Simulation Validity
03

## Slide 9
Simulation Validity
Check simulation model
Verification Test:
- We inject 28.6MeV Muon on a copper plate with settings consistent with MIXE result who did the beam test in the lab[1].
Result
- musrSim result match the experimental result.
[1] Biswas, S., Gerchow, L., Luetkens, H., Prokscha, T., Antognini, A., Berger, N., ... & Amato, A. (2022). Characterization of a continuous muon source for the Muon-Induced X-ray Emission (MIXE) Technique. arXiv preprint arXiv:2202
musrSim is a software inherited from Geant4, specified for muon research.
Geant4
Result

## Slide 10
Discussion on degrader
04

## Slide 11
Discussion on degrader
Al Fe Ti those are commonly see material for degrader.
Green for Al, Blue for Fe, Pink for Ti
With same thickness, Al is better.
Higher resolution compared to Ti
More events compared to Fe
1.Material
0. Settings
Degrader + Copper absorber + Hemisphere Detector
Result for material
Experimental Settings

## Slide 12
Discussion on degrader
2.Thickness
27.8MeV energy + Al degrader with different thickness.
High energy muon has little react on different degrader.
More background signal as thickness increase. But too thin would not stop low energy electron
Possible explanation is bremsstrahlung radiation
Muon injection
Electron injection
Bremsstrahlung radiation
A good choice is to use 5-9 mm Al degrader for surface muon detection.

## Slide 13
Detector deployment
05

## Slide 14
Detector deployment
We are going to held an experiment on SXFEL
The environment here is a complex high-background environment. We employ a statistical method to obtain potential optimal placement positions, which is different from previous quantitative optimization approaches.
Red Rectangular – SXFEL dump
Triple-layer – Detector and Absorber

## Slide 15
Detector deployment
This is det11 and det 12 who has the greatest performance which will be shown on next slides
We want to find a place possibly have a high detection efficiency.
The environment has a high background of positive and negative electron signals. For now, let's focus only on our total signal and the target signal.
Total signal : # of photons
PDG_ID==22
Target signal:# of negative muons
PDG_ID==13
We use Front and Back detectors to compare the signal-to-noise ratio before and after passing through the absorber.

## Slide 16
Detector deployment
det_11 and det_12 perform the best. And thus of det_1 indicate a more favorable position for detector placement.
Average Signal-to-noise ratio improves by 15% after passing through the Absorber.
Further position optimization and angle optimization depend on the real place situation.
Statistical Result

## Slide 17
Summary and Outlook
06

## Slide 18
Summary and Outlook
Summary
1. musrSim is Reliability verification.
2. Al plate with thickness of 5-9mm is preferable as a degrader for high energy muon incidence.
3.”Side” is a better place to deploy detector .
Outlook
1. The design will be further improved as lab experiment goes on.
2. As SHINE facility complete, higher energy and repetition rate would give a much more better result.
We are confident that one day the SHINE muon source will be successfully constructed and make a greater contribution to scientific research progress.
LaBr3
PMT